## Slide 1
Diatom Analyzer
Drop in SEM images. Get every diatom counted, measured in µm and graded intact, cracked or broken, with every pore, in one Excel file.
Runs on a laptop
Open source
No programming
W&M Nano & Biomaterials Lab · Challenge #1
Notes: One tool: images in, measurements out. Everything runs on the user's own computer.

## Slide 2
What it does
For every diatom in every image, automatically
#
Counts every diatom
Outlined and numbered on the image; touching diatoms are separated
µm
Measures it in µm
Length, width, area. Scale from the microscope file or scale bar, never assumed
∠
Reports orientation
Long-axis angle, and whether it lies face-on or on its side
✓
Grades its condition
Intact, cracked or broken, colour-coded on the image
Sp
Names its shape
Round or elongated, side view or broken piece; species once taught a few examples
•••
Measures every pore
Position and diameter of each pore, plus density and spacing
Notes: These map one-to-one onto the challenge requirements.

## Slide 3
Four steps, no programming
Double-click to start; it opens in the web browser
1
Add images
Drag in SEM images (TIF, JPG, PNG). Hitachi: add the .txt file too.
2
Pick the sample type
Diatoms apart · packed round cells · crowded, I'll mark them myself
3
Check and fix
Add a missed diatom by dragging tip to tip; remove a wrong one; set a condition; undo
4
Download
One Excel file: every diatom, every pore, a summary, and a column guide
Intact
Cracked
Broken
Edge / not assessed
Pore
Notes: Outline colours follow the condition. Every correction updates the measurements and is recorded in the spreadsheet.

## Slide 4
How it works
Classical image analysis: fast, explainable, and runs on any laptop
1
Scale
Read from the microscope's file, else the scale bar's length and label, else the tick ruler
›
2
Find
Separate diatoms from background; split touching ones; circle-finding for packed cultures
›
3
Measure
Rotated box for length and width; long-axis angle; face-on or side view
›
4
Pores
Dark spots inside each shell, sized at half their depth
›
5
Condition
Sharp inward corners and bites = broken; long crack lines or chips = cracked
›
6
Species
Match shape, size, pores and texture against a few examples per species
When it's too hard: the user marks diatoms by dragging tip to tip and the outline is traced for them. Those corrected outlines can train a Cellpose model on the lab's own images (in a test on 8 unseen crowded frames: 96 % found vs 65 % for the classical method).
Notes: Every stage is a plain rule you can inspect; all thresholds are exported with the results.

## Slide 5
How accurate: tested on unseen images
Tuned on 30 generated SEM frames, scored on 30 new frames never used for tuning
142/142
diatoms found when lying apart, no false detections
0.8 %
mean length error (scale read from the scale bar)
97 %
condition correct: intact 85/85, cracked 28/32, broken 25/25
94 → 98 %
species correct with 1 → 5 reference examples each
1.7 %
mean error in pore count per diatom
71 %
found in crowded, overlapping scenes (94 % of outlines correct)
Species: reference examples are separate specimen images; scoring uses the diatoms in the test frames (a true train / test split). Generated images have exact answers but are cleaner than real ones.
Notes: Held-out reports: reports/heldout and reports/heldout_crowded (seeds 1000-1029). Tuning frames: seeds 0-29.

## Slide 6
On the lab's own images
123 SEM images from a Phenom desktop SEM and a Hitachi S-4700
Scale: 123 / 123 read from the microscope's file. Reading the scale bar alone agrees on all 122 images where it can be checked.
✓
Works automatically
Diatoms on a clean background (Richmond pennates, 1-10 per image)
Packed Thalassiosira cultures: 90-120 valves per image in round-cell mode
Hitachi images at 3,000×: 30-45 valves each, scale from the .txt file
1-20 s per image on a laptop
!
Needs the user's help
Debris-heavy diatomite: mineral grains get outlined; remove them or mark diatoms by hand
Dense Didymosphenia fields: mark each cell by dragging tip to tip, then grade it
Close-ups of one or two cells: round-cell mode can add false circles
Real-image counting accuracy not yet measured: needs 10-20 hand-labelled images
Notes: Figures from running the app's modes over the lab folders. The fix for debris-heavy and dense scenes is a detection model trained on corrected outlines (see How it works).

## Slide 7
Try it
1
Install Python 3.10+
from python.org (once per computer)
2
Double-click the launcher
Start Diatom Analyzer (Mac).command or (Windows).bat
3
Drag in your SEM images
and download the Excel file at the end
Everything stays on your computer: no cloud, no GPU, no images uploaded. Built with open-source Python (scikit-image, OpenCV, Streamlit).